## Slide 1: Getting started with NeqSim in Matlab
Even Solbraa/Pablo Dupoy

## Slide 2: Outline
Introduction to NeqSim for Matlab
Setting up Matlab for first use of NeqSim
Select thermodynamic model, create a fluid and add components
Property calculations for single phase systems
  Reading thermodynamic properties
  Reading physical properties
Equilibrium flash calculations
  Flash calculations: TP, PH, PS, TV
  Multiphase flash
  Hydrocarbon bubble/dew point, phase envelope
  Freezing in hydrocarbon systems (LNG)
Thermodynamic calculations with water
  Thermodynamic model selection
  Water saturation, water content of a reservoir fluid
  Water, ice and hydrate dew points
Thermodynamic calculations with methanol and glycol (TEG, MEG)
  Thermodynamic model selection
  Phase equilibrium of gas, oil and glycol
  Ice, solid glycol and complex freezing points
Calculation of thermodynamic, physical and transport properties
  Density, Enthalpies, Entropies, etc.
  Viscosity, Conductivity
  Interfacial tension
  Solid adsorption
  Diffusion coefficients
Characterization of oils, PVT simulation and reservoir fluid tuning
  TBP fractions and model selection
  Defining and characterization of a fluid with a plus fractions
  PVT simulation
  PVT fluid tuning
External tools integration
  Generation of OLGA input fluids
  Generation of HYSYS fluids
Hydrate equilibrium
  Hydrate equilibrium
  Inhibitors and hydrate calculations
  Hydrate equilibrium and salts
  Top of line hydrate equilibrium
Wax and asphaltene calculations
  Prediction of wax equilibrium temperature
  Prediction of asphaltene content
Scale formation
  Adding salt and ions to fluids
  Calculation of scale formation and saturation ratio
Trace components
  Phase equilibrium of mercury in petroleum fluids
  Phase equilibrium of sulfur components (H2S, COS; RSH, S8) in petroleum fluids
Chemical equilibrium of petroleum fluids
  Chemical equilibrium in petroleum reservoirs
  Deposition, phase and chemical and equilibrium in petroleum transport and process (FeS, sulfur, HgS)
  Equilibrium in combustion processes
Thermodynamics of acid gas removal and injection
  CO2 and H2S solubility in physical solvents
  CO2 and H2S solubility in chemical solvent/alkanolamines
  Hydrocarbon solubility in solvents
  Thermodynamics of membranes for CO2/H2S removal
  Thermodynamics of cryogenic CO2 removal (freezing/distillation)
  Water solubility in CO2 and H2S and hydrocarbons
Thermodynamics of dehydration processes
  Thermodynamics of inhibition processes
  Thermodynamics of absorption of water in glycol
  Thermodynamics of water adsorption
Fluid flow
  One phase pipe flow
  Two phase pipe flow
Non-equilibrium calculations
  Simulating two-phase non equilibrium processes
  Simulating total liquid evaporation processes
  Simulating nucleation and droplet growth
Calculation of gas quality properties
  GCV, WI and relative density calculations (ISO6969)
  Gas density (AGA8) (ISO2132)
  Calculating water dew point (ISO 5198)
  Liquid density (Costald) (ISO5198)
Process simulation
  Creating streams
  Process equipment
    Valves
    Separators and scrubbers
    Compressors and pumps
    Heat exchangers
    Mixers
  Recirculation streams
  Pipelines (one-phase, two phase, multiphase)
  Absorber and distillation columns
  Working with process modules
Process design
  Pipeline design
  Design of process units (static equipment, rotary equipment, etc.)
  Designing a gas process plant
  Estimation of plot space and weight
Process economy
  Cost estimation in NeqSim
  Estimation of CAPEX and OPEX
Advanced
  Thermodynamic parameter fitting

## Slide 3: Introduction to NeqSim for Matlab
NeqSim – «Non equilibrium Simulator»1)
A tool for process and flow assurance specialist work in Statoil:
  Design of new advanced processes and equipment
  A tool for operational support
  A tool for taking R&D into business (solutions, patents, ..)
Main modules:
  Non-equilibrium and equilibrium thermodynamics
  Physical properties
  Chemical reaction equilibrium and kinetics
  Fluid mechanics
  Process simulation
  Statistics and parameter fitting
  Graphical user interface

## Slide 4: Setting up Matlab for first use of NeqSim
The NeqSim toolbox for matlab is available via GIT-hub:
https://github.com/Statoil/neqsimmatlab
To initialize calculations with NeqSim in Matlab, execute the expressions run the file:
This will make NeqSim library and database available from Matlab
Examples of Matlab scripts are found in the examples folder
  \matlab\example
pathNeqSim.m

## Slide 5: Select thermodynamic model, create a fluid
A fluid is created using the function:
  thermo(‘thermo model’, temperature, pressure)
  A thermodynamic model need to be specified
  Temperature and pressure are optional arguments
Examples of valid thermodynamic models are: pr, srk, srk-mc, cpa, umr
In the example script below, a fluid object with name fluid_1 is created, the thermodynamic model is SRK-EoS, and temperature and pressure are 10 bara and 273.15 Kelvin;
pressure = 10.0; % pressure in bara
temperature = 273.15; % temperature in Kelvin
fluid_1 = thermo(‘srk', temperature, pressure);

## Slide 6: …and add components
Valid components names can be obtained from the matlab function - componentNames
Components are added to the fluid_1 object using the method
  addComponent(component name, mole numbers)
  Where valid component names are given in the table below, and mole numbers has unit mole/second
fluid_1.addComponent('methane', 1.0); % adding 1 mole/second of methane
fluid_1.addComponent('propane', 1.0); % adding 1 mole/second of propane
Examples of valid component names:
water | CO2 | n-pentane | 3-m-C5 | 2-M-C6 | 224-TM-C5 | 3-M-C7 | 2-M-C8
MEG | methane | n-hexane | c-C5 | 23-DM-C5 | 113-TM-cy-C5 | 3-E-C6 | ethylcyclohexane
TEG | ethane | benzene | iC5 | 11-DM-cy-C5 | 22-DM-C6 | ethylbenzene | 
DEG | propane | toluene | M-cy-C5 | 3-M-C6 | E-cy-C5 | m-Xylene | 
methanol | n-butane | n-heptane | 24-DM-C5 | cis-13-DM-cy-C5 | 25-DM-C6 | p-Xylene | 
ethanol | i-butane | n-octane | 223-TM-C4 | trans-13-DM-cy-C5 | 24-DM-C6 | o-Xylene | 
nitrogen | i-pentane | c-propane | 33-DM-C5 | trans-12-DM-cy-C5 | cis-13-DM-cy-C6 | 4-M-C8 | 

## Slide 7: … and specifying mixing rule
Fluid parameters are read from the database using the function
  createDatabase(reset parameters)
  Where reset parameter is either 0 if fluid is the same as in previous calculation or 1 if all parameters should be reset. Reading new parameters will take some extra time – but if time is not limiting setting the parameter to 1 can always be used.
The mixing rule are specified using the method
  setMixingRule(mixing rule number)
  Where mixing rule number are one of:
    1. Classic all kij=0
    2. Classic using kij
    3. Classic with temperature dependent kij
    4. Huron Vidal mixing rule using NRTL GE-model (as PVTsim)
    7. CPA - classic with temperature independent kij
    9. CPA - classic with temperature dependent kij
    9. CPA - classic with composition and temperature dependent kij
fluid_1.createDatabase(1);
fluid_1.setMixingRule(2);

## Slide 8: Putting it together.. Select thermodynamic model, create a fluid and add components
pressure = 10.0; % pressure in bara
temperature = 273.15; % temperature in Kelvin
fluid_1 = thermo('srk', temperature, pressure); % using the SRK-EoS
fluid_1.addComponent('methane', 1.0); % adding 1 mole/second of methane
fluid_1.addComponent('propane', 1.0); % adding 1 mole/second of propane
fluid_1.createDatabase(1); % reading new parameters from database
fluid_1.setMixingRule(2); % using classic mixing rule with kij

## Slide 9: Property calculations for single phase systems
If a fluid is know to have only one phase – with known phase type (gas or liquid), calculations of properties is done using the method:
  fluidName.init(1/2/3)
  init(1) – will calculate volume/density and fugasity coefficients
  init(2) – will calculate additinally to init(1) calculate temperature and pressure derivatives of fugacity coefficients
  init(3) – will additionally to init(2) calculate compsitional derivatives, such as derivative of fugacity with respect to composition
On a one phase systems – the number and type of phase has to be set
If physical properties (viscosity, conductivity, etc.) are needed the methods: fluidName.initPhysicalProperties() has to be called befor retreieving the properties.
pressure = 10.0; % pressure in bara
temperature = 273.15; % temperature in Kelvin
fluid_1 = thermo('srk', temperature, pressure); % using the SRK-EoS
fluid_1.addComponent('methane', 1.0); % adding 1 mole/second of methane
fluid_1.addComponent('propane', 1.0); % adding 1 mole/second of propane
fluid_1.createDatabase(1); % reading new parameters from database
fluid_1.setMixingRule(2); % using classic mixing rule with kij
fluid_1.init(0); % a fluid need to be initialized using init(0)
fluid_1.setNumberOfPhases(1) % setting number of phases to one
fluid_1.setPhaseType(0,1) % setting first phase (0) to be of type gas (1)/liquid(0)
fluid_1.init(3); % calculates properties of the fluid
fluid_1.getPhase(0).getEnthalpy(); % reads the enthalpy
fluid_1.initPhysicalProperties(); % calculates physical properties
fluid_1.getPhase(0).getPhysicalProperties().getViscosity() % returns the calculated viscosity

## Slide 10: Reading thermodynamic properties [can be read after calling init(1/2/3)]
fluid_1.getPhase(0).getEnthalpy(); – enthalpy with unit J
fluid_1.getPhase(0).getComponent(‘methane’).getx(); - get molefraction of methane in phase 0
fluid_1.getPhase(‘gas’).getComponent(0).getx(); - get molefraction of component number 0 (first added component) in gas phase
fluid_1.getPhase(‘gas’).getComponent(0).getz(); - get total feed fraction of component number 0 (first added component)
fluid_1.getPhase(0).getComponent(0).getNumberOfMolesInPhase(); - get number of moles of methane in phase 0
fluid_1.getPhase(0).getComponent(0).getNumberOfMoles(); - get number of moles of component 0 in total fluid
fluid_1.getPhase(0).getZ(); - get compressibility factor of phase 0 fluid_1.getPhase(0).getVolume(); - get volume of phase 0 (unit m^3/1e5)
fluid_1.getVolume(); - get volume of fluid (unit m^3/1e5)
fluid_1.getPhase(0).getComponent(0).getFugicityCoefficient(); - get fugacity coeffisient of component 0 in first phase
fluid_1.getPhase(0).getComponent(0).getdfugdt(); - get derivative of ln fugacity coeffisient of component 0 with respect to temperature
fluid_1.getPhase(0).getComponent(0).getdfugdp - get derivative of ln fugacity coeffisient of component 0 with respect to pressure
fluid_1.getPhase(0).getComponent(0).getdfugdn(0) - get derivative of ln fugacity coeffisient of component 0 with respect to molnumer of component number 1
All available methods for an object can be found by the Matlab function methods(oject) – eg. methods(fluid_1)
getEntropy() - entropy with unit J/molK
getInternalEnergy() - internal energy
getZ()

## Slide 11: Reading physical properties [can be read after calling initPhysicalProperties()]
fluid_1.getPhase(0).getPhysicalProperties().getViscosity() - calculated viscosity of phase 0
fluid_1.getPhase(0).getPhysicalProperties().getDensity() - calculated density of phase 0
fluid_1.getPhase(0).getPhysicalProperties().getConductivity() - calculated density of phase 0
fluid_1.getPhase(0). getInterphaseProperties().getInterfacialTension(0,1) - calculated interfacial tension between phase 0 and phase 1
fluid_1.getPhase(0). getInterphaseProperties().getEffectiveDIffusionCoefficient(0)- calculated effective diffusion coefficient of component 0 in phase 1

## Slide 12: Equilibrium flash calculations
Flash calculations: TP, PH, PS, TV
Multiphase flash
Bubble/dew point, phase envelope

## Slide 13: Equilibrium flash calculations
Flash calculations: TP, PH, PS, TV
Multiphase flash
Bubble/dew point, phase envelope

## Slide 14: Equilibrium flash caculations
Flash calculation at constant temperature and pressure is done using the function
  TPflash(fluid);
A table with selected fluid properties can be presented graphically by typing the fluid name without a semicolon (see figure)
TPflash(fluid_1);
fluid_1

## Slide 15: Flash calculation sepcifications
Specification 1 | Specification 2 | Method name
Temperature | Pressure | TPflash(fluid name)
Pressure | Enthalpy | PHflash(fluid name, enthalpy)
Pressure | Entropy | PSflash(fluid name, entropy)
Temperature | Volume | TVflash(fluid name, volume)
Example of a combination of a temperature-pressure and a pressure-enthalpy flash:
pressure = 10.0; % pressure in bara
temperature = 273.15; % temperature in Kelvin
fluid_1 = thermo('srk', temperature, pressure); % using the SRK-EoS
fluid_1.addComponent('methane', 1.0); % adding 1 mole/second of methane
fluid_1.addComponent('propane', 1.0); % adding 1 mole/second of propane
fluid_1.createDatabase(1); % reading new parameters from database
fluid_1.setMixingRule(2); % using classic mixing rule with kij
TPflash(fluid_1) % doing a flash at constant pressure and temperature
initialEnthalpy = fluid_1.getEnthalpy; % reading enthalpy of fluid
fluid_1.setPressure(1.0); % setting pressure to 1.0 bara
PHflash(fluid_1, initialEnthalpy); % doing a flash at given enthalpy and pressure
fluid_1.getTemperature % reading resulting temperature
Link: TP_PH_flash.m

## Slide 16: Multiphase flash calculations
By default NeqSim will have a maximum of two fluid phases (gas/liquid)
In many cases in oil industry we will need to calculate equilibrium involving three fluid phases- A typical situation will be when we have a gas, oil and a water phase
A multiphase calculation is more computational demanding calculations – and the speed of calculations will be reduced
To turn on the mulitphase calculation option, use the command
  setMultiPhaseCheck(0/1) - where 0 is off and 1 is on
pressure = 10.0; % pressure in bara
temperature = 273.15; % temperature in Kelvin
fluid_1 = thermo('srk', temperature, pressure); % using the SRK-EoS
fluid_1.addComponent('methane', 1.0); % adding 1 mole/second of methane
fluid_1.addComponent('n-heptane', 1.0); % adding 1 mole/second of n-heptane
fluid_1.addComponent('water', 1.0); % adding 1 mole/second of water
fluid_1.createDatabase(1); % reading new parameters from database
fluid_1.setMixingRule(2); % using classic mixing rule with kij
fluid_1.setMultiPhaseCheck(1) % specifies that calculations should check for more than two fluid phases
TPflash(fluid_1) % doing a multi phase flash at constant pressure and

## Slide 17: Hydrocarbon bubble/dew point, phase envelopes
The recomended thermodynamic model for calculating hydrocarbon dew points is the UMR-PRU model.
This model is selected in neqsim using the method: thermo('UMR-PRU-EoS',temperature, pressure);
pressure = 35.0; % pressure in bara
temperature = 273.15; % temperature in Kelvin
fluid_1 = thermo('UMR-PRU-EoS', temperature , pressure ); % using the UMR-PRU model
fluid_1.addComponent('CO2', 3.0);
fluid_1.addComponent('methane', 90.0);
fluid_1.addComponent('ethane', 5.0);
fluid_1.addComponent('propane', 3.0);
fluid_1.createDatabase(1); % reading new parameters from database
fluid_1.setMixingRule('HV', 'UNIFAC_UMRPRU'); % using the mixing rule defined for UMR-PRU¨
dewt(fluid_1); % calculating dew point of fluid
bubt(fluid_1); % calculating bublepoint temperature of fluid
phaseenvelope(fluid_1); % calculating phase envelope of fluid

## Slide 18: Freezing in hydrocarbon systems (LNG)
Soid formation temperature can be calculated for CO2, methane, ethane, propane, benzene, toluene, c-hexane, etc.
Freezing can be a components in low temperatures can be simulatid using the method: freezet(component name)
pressure = 35.0; % pressure in bara
temperature = 123.15; % temperature in Kelvin
fluid_1 = thermo(‘UMR-PRU-EoS', temperature , pressure ); % using the UMR-PRU model
fluid_1.addComponent('CO2', 0.01);
luid_1.addComponent('methane', 100.0);
fluid_1.createDatabase(1); % reading new parameters from database
freezet(‘CO2’); % calculating freezing point temperatue of CO2

## Slide 19: Thermodynamic calculations with water
Thermodynamic model selection
Water saturation, water content of a reservoir fluid
Hydrate equilibrium
Water, ice and hydrate dew points

## Slide 20: Thermodynamic model selection for mixtures containing water
During the last 15 years advanced and more accurate models have been developed for thermodynamic calulcations involving polar components.
Statoil has been active in the development of the CPA-EoS (cubic plus assciation)
The CPA-EoS is the recomended thermodunamic model i Statoil for doing calculations such as:
  Water content of gas and oil
  Hydrate equilibrium in complex fluid mixtures (eg. low water content fluids)
  Distribution of chemicals (such as glycols) in gas and oil
The CPA-model is selected by specifying the model: thermo(‘cpa’, temperature, pressure)
By specifying the mixing rule choice as number 9, the classic mixing rule with temperature dependent kij is used

## Slide 21: Water saturation – calculating water content of a reservoir fluid
Saturating of a gas with water is done using the function saturateWithWater(fluidName)
The fluid will be saturated with water at current temperature and pressure of the fluid
reservoirPressure = 210.0; % pressure in bara
treservoirTemperature = 373.15; % temperature in Kelvin
fluid_1 = thermo(‘cpa', treservoirTemperature , reservoirPressure ); % using the CPA-EoS
fluid_1.addComponent(‘CO2', 3.0);
luid_1.addComponent('methane', 90.0);
fluid_1.addComponent(‘ethane', 5.0);
fluid_1.addComponent(‘propane', 3.0);
fluid_1.createDatabase(1); % reading new parameters from database
fluid_1.setMixingRule(9); % using classic mixing rule with temperature dep. kij
saturateWithWater(fluid_1) % saturating the gas with water

## Slide 22: Water, ice and hydrate dew points
In the natral gas industry we normally define the water dew point as the first water rich phase that drops out of a gas. This can be aqueous water, ice or gas hydrate.
The calculation of water dew points are done using the mehods
  waterDewt(fluidName) – for aqueous dew point
  hydt(fluidName) – for natural gas hydrate formation
  Freezt(fluidName, ‘water’) – for checking ice formation temperature
waterDewt(fluid_1); % calculating aqueous water dew point temperature
hydt(fluid_1); % calculating the hydrate equilibrim temperature
freezt(fluid_1, ‘water’); % calculation of ice formation temperature

## Slide 23: Thermodynamic calculations with methanol and glycol (TEG, MEG)
The following glycols and alcohols are implemented in NeqSim
  Glycols: MEG, TEG, DEG, TREG
  Alcohols: methanol, ethanol
Mixtures of water, glycols and alcohols can also be used

## Slide 24: Thermodynamic model selection for systems containing glycol and alcohols
As for calculation involving water – the prefered model for phase equilibrium involving glycols or alcohols suc as methanol, will be the CPA-EoS
The model sould be able to calculate distributin of water, glycols and alcohols with good accuracy

## Slide 25: Phase equilibrium of gas, oil and glycol
An example of a phase equilibrium calculation of gas, liquid hydrocarbon and MEG and water is illustrated below
pressure = 100.0; % pressure in bara
temperature = 293.15; % temperature in Kelvin
fluid_1 = thermo(‘cpa', temperature , pressure ); % using the CPA-EoS
fluid_1.addComponent(‘CO2', 3.0);
luid_1.addComponent('methane', 90.0);
fluid_1.addComponent(‘ethane', 5.0);
fluid_1.addComponent(‘propane', 3.0);
fluid_1.addComponent(‘n-nonane', 3.0); % adding heavy hydrocarbon component
fluid_1.addComponent(‘MEG', 10.0);
fluid_1.addComponent(‘water', 90.0);
fluid_1.createDatabase(1); % reading new parameters from database
fluid_1.setMixingRule(9); % using classic mixing rule with temperature dep. kij
fluid_1.setMultiPhaseCheck(1); % setting the algorithm to check for more than two phases
TPflash(fluid_1); % performing a TP-flash calculation

## Slide 26: Ice, solid glycol, alcohols and complex freezing points
Formation of ice, solid glycol and complex solids (combination of water – alcohol/glycol) can be done
The method used for calculating solid formation of glycols and alcohols is freezt(fluidName, componentName)
The complex phase is calcuated using the method solidComplexT(fluidName, ‘complex component 1’, ‘complex component 2’)
  The implemented complexes are MEG-water, TEG-water, methanol-water
Hydrate temeprature is calculated using hydt(fluid)
TPflash(fluid_1); % performing a TP-flash calculation
freezt(fluidName, ‘sold component name’) % calculates solid formation temperature
solidComplexT(fluid_1, ‘MEG’, ‘water’) % cakculates the solid complex formation temperature of MEG-water

## Slide 27: Calculation of thermodynamic, physical and transport properties
A numer of physical and transport properties can be calculated using NeqSim. Examples of such properties are:
  Densities
  Viscosities
  Conductivities
  Diffusivities
  Interfacial tension
  Solid surface adsorption properties
A number of methods are available for calculating the various properties

## Slide 28: Density, Enthalpy, Entropy, etc.
The density of a fluid can be obtained in two ways:
  fluidName.getPhase(phaseNumber).getPhysicalProperties().getDensity()
  density(fluidName) – returns an aray of denisties for a mulit phase system
The enthalp and entropy are obtained from the functions:
  fluidName.getEnthalpy, fluidName.getEntropy - returns total enthalpy/entropy
  fluidName.getPhase(phaseNumber).getEnhalpy - returns enthalpy/entropy for a given phase
pressure = 10.0; % pressure in bara
temperature = 273.15; % temperature in Kelvin
fluid_1 = thermo('srk', temperature, pressure); % using the SRK-EoS
fluid_1.addComponent('methane', 1.0); % adding 1 mole/second of methane
fluid_1.addComponent(‘n-heptane', 1.0); % adding 1 mole/second of n-heptane
fluid_1.createDatabase(1); % reading new parameters from database
fluid_1.setMixingRule(2); % using classic mixing rule with kij
TPflash(fluid_1) % doing a TPflash at constant pressure and temperature
fluid_1.getEnthalpy; % reads total Enthalpy (unit is J/mol)
fluid_1.getEntropy; % reads total Entropy
fluid_1.getPhase(0).getEntropy % read entropy of first phase (gas in this case)
flluid_1.getPhase(0).getPhysicalProperties().getDensity %reads density of first phase unit is kg/m^3

## Slide 29: Viscosity, Conductivity
Viscosity and conductivity is obtained using the functions
  getViscosity(), getConductivity()

## Slide 30: Interfacial tension
Surface tension between phase 0 and 1 is calculated from method: fluid_1.getInterphaseProperties().getSurfaceTension(0, 1)
Various surface tension methods are available (parachor method, gradient theory, etc.). They method to be used are set by: fluid_1.getInterphaseProperties().setInterfacialTensionModel(0/1/2); where 0 is parachor method, 1 is gradient theory and 2 is linear gradient theory

## Slide 31: Solid adsorption
Adsorption of gas on a solid material (kg component/kg material) is calculated by methods:
fluid_1.getInterphaseProperties().initAdsorption(); fluid_1.getInterphaseProperties().setSolidAdsorbentMaterial("AC"); % Activated carbon Norit R1 fluid_1.getInterphaseProperties().calcAdsorption();

## Slide 32: Diffusion coefficients

## Slide 33: Characterization, PVT simulation and reservoir fluid tuning
NeqSim have implemented a number of characterisation methods for the available equation of states
Typically a fluid consists of standard defined components, pseudo components (oil fractions) and eventually a plus fraction component
The characterization method will dstiribute components into a number of boiling point fraction (TBP-fractions). As default twelve TBP fractions are used.
The properties of TBP fractions are calculted using vaius methods relating critical properties (Tc, Pc, acentric factor) to molar mass and density of the fraction.

## Slide 34: TBP fractions and model selection
A pseudocomponent (true boiling point fraction) is added to a fluid using the method: addTPBfraction(‘fraction name’, numer of moles, molar mass, density) the unit for molar mass is kg/mol and density is gr/cm^3
The method used for characterization of TBP fractions is set by: fluidName.getCharacterization().setTBPModel(‘PedersenSRK’); Available options are ,RiaziDaubert, PedersenPR, PedersenSRK.
pressure = 10.0; % pressure in bara
temperature = 273.15; % temperature in Kelvin
fluid_1 = thermo('srk', temperature, pressure); % using the SRK-EoS
fluid_1.getCharacterization().setTBPModel(‘PedersenSRK’); % setting characterization method (method to calculate Tc, Pc, omega
fluid_1.addComponent('methane', 10.0); % adding 1 mole/second of methane
fluid_1.addTBPfraction(‘C7', 1.0, 0.102, 0.81); % adding 1 mole/second of a pseudo component C7
fluid_1.addTBPfraction(‘C8', 0.4, 0.112, 0.83); % adding 1 mole/second of a pseudo component C8
fluid_1.addTBPfraction(‘C9', 0.2, 0.132, 0.84); % adding 1 mole/second of a pseudo component C9
fluid_1.createDatabase(1); % reading parameters from database
fluid_1.setMixingRule(2); % using classic mixing rule with kij
TPflash(fluid_1) % doing a TPflash at constant pressure and temperature\

## Slide 35: Defining and characterization of a fluid with a plus fractions
A plus fraction component is set by the method addPlusFraction(‘fraction name’, numer of moles, molar mass, density)
The lumping method is set by the method: fluidName.getCharacterization().setLumpingModel(‘no’); available options are: no/ab lumping/pedersen
The number of lumped components are set by the method: fluidName.getCharacterization().getLumpingModel().setNumberOfLumpedComponents(number);
Characterization of the fluid is done by calling the method: fluidName.getCharacterization().characterisePlusFraction();
pressure = 10.0; % pressure in bara
temperature = 273.15; % temperature in Kelvin
fluid_1 = thermo('srk', temperature, pressure); % using the SRK-EoS
fluid_1.getCharacterization().setTBPModel(‘PedersenSRK’); % setting characterization method (method to calculate Tc, Pc, omega) fluid_1.getCharacterization().setLumpingModel(‘pedersen’) % setting lumping model to pedersen
fluid_1.getCharacterization().getLumpingModel().setNumberOfLumpedComponents(8); % set number of lumped components to 8
fluid_1.addComponent('methane', 10.0); % adding 1 mole/second of methane
fluid_1.addTBPfraction(‘C7', 1.0, 0.102, 0.81); % adding 1 mole/second of a pseudo component C7
fluid_1.addTBPfraction(‘C8', 0.4, 0.112, 0.83); % adding 1 mole/second of a pseudo component C8
fluid_1.addTBPfraction(‘C9', 0.2, 0.132, 0.84); % adding 1 mole/second of a pseudo component C9
fuid_1.addPlusFraction(‘C10’, 1.0, 0.190, 0.87); %adding plus fraction C10+
fluid_1.createDatabase(1); % reading parameters from database
fluid_1.setMixingRule(2); % using classic mixing rule with kij
fluid_1.getCharacterization().characterisePlusFraction(); % characterisation of the fluid
TPflash(fluid_1) % doing a TPflash at constant pressure and temperature\

## Slide 36: PVT simulation
Various types of PVT simulation calculations are implemented in NeqSim:
  Constand volume depletion
  Constant mass depletion
  Saturation pressure simulation
  Separator test simulation
  Slim tube simulation
pressure = 10.0; % pressure in bara
temperature = 273.15; % temperature in Kelvin
fluid_1 = thermo('srk', temperature, pressure); % using the SRK-EoS
fluid_1.getCharacterization().setTBPModel(‘PedersenSRK’); % setting characterization method (method to calculate Tc, Pc, omega) fluid_1.getCharacterization().setLumpingModel(‘pedersen’) % setting lumping model to pedersen
fluid_1.getCharacterization().getLumpingModel().setNumberOfLumpedComponents(8); % set number of lumped components to 8
fluid_1.addComponent('methane', 10.0); % adding 1 mole/second of methane
fluid_1.addTBPfraction(‘C7', 1.0, 0.102, 0.81); % adding 1 mole/second of a pseudo component C7
fluid_1.addTBPfraction(‘C8', 0.4, 0.112, 0.83); % adding 1 mole/second of a pseudo component C8
fluid_1.addTBPfraction(‘C9', 0.2, 0.132, 0.84); % adding 1 mole/second of a pseudo component C9
fuid_1.addPlusFraction(‘C10’, 1.0, 0.190, 0.87); %adding plus fraction C10+
fluid_1.createDatabase(1); % reading parameters from database
fluid_1.setMixingRule(2); % using classic mixing rule with kij
fluid_1.getCharacterization().characterisePlusFraction(); % characterisation of the fluidConstantVolumeDepletion(tempSystem)
constantVolumeDepletion(fluid_1); % Constant volume depletion simulation constantMassDepletion(fluid_1); % constant mass depletion saturationPressure(fluid_1); % saturation pressure

## Slide 37: PVT fluid tuning
Tuning of a fluid to PVT data can be done using the NeqSim implemented PVTtuning functions. Example of use of the tuning function are illustrated below for tuning to saturation temperature and pressure (eg. Reservoir conditions)
pressure = 10.0; % pressure in bara
temperature = 273.15; % temperature in Kelvin
fluid_1 = thermo('srk', temperature, pressure); % using the SRK-EoS
fluid_1.getCharacterization().setTBPModel(‘PedersenSRK’); % setting characterization method (method to calculate Tc, Pc, omega) fluid_1.getCharacterization().setLumpingModel(‘pedersen’) % setting lumping model to pedersen
fluid_1.getCharacterization().getLumpingModel().setNumberOfLumpedComponents(8); % set number of lumped components to 8
fluid_1.addComponent('methane', 10.0); % adding 1 mole/second of methane
fluid_1.addTBPfraction(‘C7', 1.0, 0.102, 0.81); % adding 1 mole/second of a pseudo component C7
fluid_1.addTBPfraction(‘C8', 0.4, 0.112, 0.83); % adding 1 mole/second of a pseudo component C8
fluid_1.addTBPfraction(‘C9', 0.2, 0.132, 0.84); % adding 1 mole/second of a pseudo component C9
fuid_1.addPlusFraction(‘C10’, 1.0, 0.190, 0.87); %adding plus fraction C10+
fluid_1.createDatabase(1); % reading parameters from database
fluid_1.setMixingRule(2); % using classic mixing rule with kij
fluid_1.getCharacterization().characterisePlusFraction(); % characterisation of the fluidConstantVolumeDepletion(tempSystem)
sattuning = saturationPressure(fluid_1); % initiating saturation pressure simulation
sattuning.setSaturationConditions(saturationTemperature, saturationPressure); % setting saturation pressure and temperature
sattuning.run(); % running tuning of fluid (default is to tune molecular mass of plus fraction)

## Slide 38: Hydrate modelling with NeqSim
NeqSim is well suited for doing hydrate prediction in systems of water ,inhibitors and salts
The models implemented are based on the CPA-EoS combined with a hydrate model

## Slide 39: Hydrate equilibrium calculations
Hydrate equilibrium temperature calculation for a fluid is done using the function hydt(fluidName)
The fluid has to be initialized to check for hydrates. This is done using the function setHydrateCheck(0/1) – 0 means do not check for hydrates and 1 means check for hydrates
reservoirPressure = 210.0; % pressure in bara
treservoirTemperature = 373.15; % temperature in Kelvin
fluid_1 = thermo(‘cpa', treservoirTemperature , reservoirPressure ); % using the CPA-EoS
fluid_1.addComponent(‘CO2', 3.0);
luid_1.addComponent('methane', 90.0);
fluid_1.addComponent(‘ethane', 5.0);
fluid_1.addComponent(‘propane', 3.0);
fluid_1.createDatabase(1); % reading new parameters from database
fluid_1.setMixingRule(9); % using classic mixing rule with temperature dep. kij
saturateWithWater(fluid_1); % saturating the gas with water
fluid_1.setHydrateCheck(1); % initializing the fluid to check for hydrates
fluid_1.setMultiPhaseCheck(1); % setting the algorithm to check for more than two phases
hydt(fluid_1); % calculating the hydrate equilibrim temperature

## Slide 40: Hydrate equilibrium calculations with inhibitors
NeqSim is well suited for performing hydrate calulcations and evaluating the effect of adding inhibitors like glycols or alcohols
Hydrate equilibrium temperature is calculated using hydt(fluid). Hydrate equilibrium pressure is calculated using hydp(fluidName)
The calculated structure can be obtained usin the function: fluid.getPhase(‘hydrate’).getHydrateStructure()
pressure = 100.0; % pressure in bara
temperature = 293.15; % temperature in Kelvin
fluid_1 = thermo(‘cpa', temperature , pressure ); % using the CPA-EoS
fluid_1.addComponent(‘CO2', 3.0);
luid_1.addComponent('methane', 90.0);
fluid_1.addComponent(‘ethane', 5.0);
fluid_1.addComponent(‘propane', 3.0);
fluid_1.addComponent(‘n-nonane', 3.0); % adding heavy hydrocarbon component
fluid_1.addComponent(‘MEG', 10.0);
fluid_1.addComponent(‘water', 90.0);
fluid_1.createDatabase(1); % reading new parameters from database
fluid_1.setMixingRule(9); % using classic mixing rule with temperature dep. kij
fluid_1.setMultiPhaseCheck(1); % setting the algorithm to check for more than two phases
fluid_1.setHydrateCheck(1); % initializing the fluid to check for hydrates
hydt(fluid_1); % performing a TP-flash calculation
fluid_1.getPhase(‘hydrate’).getHydrateStructure % read hydrate structure

## Slide 41: Hydrate equilibrium calculations with salts
Salts are added to the system using the function: addSalt(‘NaCl’, moles);
pressure = 100.0; % pressure in bara
temperature = 293.15; % temperature in Kelvin
fluid_1 = thermo(‘cpa', temperature , pressure ); % using the CPA-EoS
fluid_1.addComponent(‘CO2', 3.0);
luid_1.addComponent('methane', 90.0);
fluid_1.addComponent(‘ethane', 5.0);
fluid_1.addComponent(‘propane', 3.0);
fluid_1.addComponent(‘n-nonane', 3.0); % adding heavy hydrocarbon component
fluid_1.addComponent(‘MEG', 10.0);
fluid_1.addComponent(‘water', 90.0);
fluid_1.addSalt(‘NaCl', 0.1); % adding salt 0.1 mole/sec
fluid_1.createDatabase(1); % reading new parameters from database
fluid_1.setMixingRule(9); % using classic mixing rule with temperature dep. kij
fluid_1.setMultiPhaseCheck(1); % setting the algorithm to check for more than two phases
fluid_1.setHydrateCheck(1); % initializing the fluid to check for hydrates
hydt(fluid_1); % performing a TP-flash calculation
fluid_1.getPhase(‘hydrate’).getHydrateStructure % read hydrate structure

## Slide 42: Top of line hydrate equilibrium
Top of line hydrate equilibrium temperature is calculated using function: hydt_TOL(fluidname)
pressure = 100.0; % pressure in bara
temperature = 293.15; % temperature in Kelvin
fluid_1 = thermo(‘cpa', temperature , pressure ); % using the CPA-EoS
fluid_1.addComponent(‘CO2', 3.0);
luid_1.addComponent('methane', 90.0);
fluid_1.addComponent(‘ethane', 5.0);
fluid_1.addComponent(‘propane', 3.0);
fluid_1.addComponent(‘n-nonane', 3.0); % adding heavy hydrocarbon component
fluid_1.addComponent(‘MEG', 10.0);
fluid_1.addComponent(‘water', 90.0);
fluid_1.createDatabase(1); % reading new parameters from database
fluid_1.setMixingRule(9); % using classic mixing rule with temperature dep. kij
fluid_1.setMultiPhaseCheck(1); % setting the algorithm to check for more than two phases
fluid_1.setHydrateCheck(1); % initializing the fluid to check for hydrates
hydt_TOL(fluid_1); % calculates top of line hydrate formation temperature

## Slide 43: Wax and asphaltene calculations
The simlified PC-SAFT equation of stat is recomended for doing wax calculations in NeqSim. The method is beleived to be accurate for long chained parafinic hydrocarbons. The simlified PC-SAFT method is selectd by spesifying:
pressure = 10.0; % pressure in bara
temperature = 273.15; % temperature in Kelvin
fluid_1 = thermo(‘sPC-SAFT', temperature, pressure);
Asphaltene calculations can be done be selecting the SRK-EoS (no special recomended model for asphaltene precipitation at the moment)

## Slide 44: Wax calculations
Thermodynamics of wax are simulated following the methods of Pedersen et. al.
Wax calculations need to be initiated using the method: fluidName.addTBPWax(); - to split the fractions up in wax formers and non-wax fluidName.addSolidComplexPhase("wax");
Wax equilibrium temperature is calculated using the method: waxt(fluidName);
pressure = 10.0; % pressure in bara
temperature = 273.15; % temperature in Kelvin
fluid_1 = thermo('srk', temperature, pressure); % using the SRK-EoS
fluid_1.getCharacterization().setTBPModel(‘PedersenSRK’); % setting characterization method (method to calculate Tc, Pc, omega) fluid_1.getCharacterization().setLumpingModel(‘pedersen’) % setting lumping model to pedersen
fluid_1.getCharacterization().getLumpingModel().setNumberOfLumpedComponents(8); % set number of lumped components to 8
fluid_1.addComponent('methane', 10.0); % adding 1 mole/second of methane
fluid_1.addTBPfraction(‘C7', 1.0, 0.102, 0.81); % adding 1 mole/second of a pseudo component C7
fluid_1.addTBPfraction(‘C8', 0.4, 0.112, 0.83); % adding 1 mole/second of a pseudo component C8
fluid_1.addTBPfraction(‘C9', 0.2, 0.132, 0.84); % adding 1 mole/second of a pseudo component C9
fuid_1.addPlusFraction(‘C10’, 1.0, 0.190, 0.87); %adding plus fraction C10+
fluid_1.createDatabase(1); % reading parameters from database
fluid_1.getCharacterization().characterisePlusFraction(); % characterisation of the fluidConstantVolumeDepletion(tempSystem)
fluid_1.addTBPWax(); % Splitting up TBPfraction in to wax formers and non wax formers
fluid_1.setMixingRule(2); % using classic mixing rule with kij
fluid_1.addSolidComplexPhase(‘wax’); % adding the possibility to simulating waxphases
waxt(fluid_1); % calculating wax equilibrium formation temperature

## Slide 45: Prediction of asphaltene content
To be implemented……..

## Slide 46: Non-equilibrium calculations
Non-equilibrium calculations are calculted using the non-equilibrium multipase model developed for NeqSim
The same base model is used for all non-equilibrium simulations
Examples of such calculations are evaporation and condensation processes

## Slide 47: Simulating two-phase non equilibrium processes
A fluid is reated adding components to invidual phases using fluid.addComponent(componentName, moles/Sec, phase)
A pipe is created using pipe(innerDiameter, length)
Evaporation is modeled using the function neqsim(fluid, pipe, flowtype) - flow type can be selected to auto
pressure = 10.0; % pressure in bara
temperature = 273.15; % temperature in Kelvin
fluid_1 = thermo('srk', temperature, pressure); % using the SRK-EoS
fluid_1.getCharacterization().setTBPModel(‘PedersenSRK’); % setting characterization method (method to calculate Tc, Pc, omega
fluid_1.addComponent('methane', 10.0, 0); % adding 1 mole/second of methane to phase 0 (gas)
fluid_1.addTBPfraction(‘C7', 1.0, 0.102, 0.81, 1); % adding 1 mole/second of a pseudo component C7 to phase 1 (liquid)
fluid_1.addTBPfraction(‘C8', 0.4, 0.112, 0.83, 1); % adding 1 mole/second of a pseudo component C8 to phase 1 (liquid)
fluid_1.addTBPfraction(‘C9', 0.2, 0.132, 0.84, 1); % adding 1 mole/second of a pseudo component C9 to phase 1 (liquid)
fluid_1.createDatabase(1); % reading parameters from database
fluid_1.setMixingRule(2); % using classic mixing rule with kij
pipe = pipe(1.0, 100.0); % creating a pipe with inner diameter 1.0 and length 100 meter
sim = neqsim(fluid_1, pipe, ‘droplet’); % simulates a non equilibrium process of the fluid In the pipe
sim.run % running calculation
sim.display % displaying results

## Slide 48: Simulating total liquid evaporation processes
A total evoparation process means that the fluid will be one phase at equilibrium
A typical example can be evaporation of water into a dry gas
pressure = 10.0; % pressure in bara
temperature = 273.15; % temperature in Kelvin
fluid_1 = thermo('srk', temperature, pressure); % using the SRK-EoS
fluid_1.getCharacterization().setTBPModel(‘PedersenSRK’); % setting characterization method (method to calculate Tc, Pc, omega
fluid_1.addComponent('methane', 10.0, 0); % adding 1 mole/second of methane to phase 0 (gas)
fluid_1.addTBPfraction(‘C7', 0.01, 0.102, 0.81, 1); % adding 1 mole/second of a pseudo component C7 to phase 1 (liquid))
fluid_1.createDatabase(1); % reading parameters from database
fluid_1.setMixingRule(2); % using classic mixing rule with kij
pipe = pipe(1.0, 100.0); % creating a pipe with inner diameter 1.0 and length 100 meter
sim = neqsim(fluid_1, pipe, ‘droplet’); % simulates a non equilibrium process of the fluid In the pipe
sim.run % running calculation
sim.display % displaying results

## Slide 49: Simulating nucleation and droplet growth
Nucleation is the process where a new phase are created. It can be homoenious (in fluid) or hetrogeneous (in surface) nucleation
The simulation has to be initiated using flow type ‘droplet nucleation’
pressure = 10.0; % pressure in bara
temperature = 273.15; % temperature in Kelvin
fluid_1 = thermo('srk', temperature, pressure); % using the SRK-EoS
fluid_1.getCharacterization().setTBPModel(‘PedersenSRK’); % setting characterization method (method to calculate Tc, Pc, omega
fluid_1.addComponent('methane', 10.0, 0); % adding 1 mole/second of methane to phase 0 (gas)
fluid_1.addTBPfraction(‘C7', 0.01, 0.102, 0.81, 0); % adding 1 mole/second of a pseudo component C7 to phase 1 (liquid))
fluid_1.addTBPfraction(‘C7', 0.01, 0.102, 0.81, 0); % adding 1 mole/second of a pseudo component C7 to phase 1 (liquid))
fluid_1.createDatabase(1); % reading parameters from database
fluid_1.setMixingRule(2); % using classic mixing rule with kij
pipe = pipe(1.0, 100.0); % creating a pipe with inner diameter 1.0 and length 100 meter
sim = neqsim(fluid_1, pipe, ‘’droplet nucleation’); % simulates a non equilibrium process of the fluid In the pipe
sim.run % running calculation
sim.display % displaying results

## Slide 50: Calculation of gas quality properties
Gas quality parameters such as heating values (GCV), Wobbe index (WI) and relative densities are calculated accurding to ISO6976-2005
Other gas quality parameters such as dew points (water, hydrocarbons) can also be calculated

## Slide 51: TBP fractions and model selection
A pseudocomponent (true boiling point fraction) is added to a fluid using the method: addTPBfraction(‘fraction name’, numer of moles, molar mass, density) the unit for molar mass is kg/mol and density is gr/cm^3
The method used for characterization of TBP fractions is set by: fluidName.getCharacterization().setTBPModel(‘PedersenSRK’); Available options are ,RiaziDaubert, PedersenPR, PedersenSRK.
pressure = 10.0; % pressure in bara
temperature = 273.15; % temperature in Kelvin
fluid_1 = thermo('srk', temperature, pressure); % using the SRK-EoS
fluid_1.getCharacterization().setTBPModel(‘PedersenSRK’); % setting characterization method (method to calculate Tc, Pc, omega
fluid_1.addComponent('methane', 10.0); % adding 1 mole/second of methane
fluid_1.addTBPfraction(‘C7', 1.0, 0.102, 0.81); % adding 1 mole/second of a pseudo component C7
fluid_1.addTBPfraction(‘C8', 0.4, 0.112, 0.83); % adding 1 mole/second of a pseudo component C8
fluid_1.addTBPfraction(‘C9', 0.2, 0.132, 0.84); % adding 1 mole/second of a pseudo component C9
fluid_1.createDatabase(1); % reading parameters from database
fluid_1.setMixingRule(2); % using classic mixing rule with kij
TPflash(fluid_1) % doing a TPflash at constant pressure and temperature\

## Slide 52: GCV, WI and relative density calculations (ISO6976-2005)
GCV are calculated using the method GCV(fluidName, volume reference temperature, combustion reference temperature)
WI are calculated using the method WI(fluidName, volume reference temperature, combustion reference temperature)
Relative density are caluated using: reldens(fluidName, volume reference temperature)
pressure = 35.0; % pressure in bara
temperature = 273.15; % temperature in Kelvin
fluid_1 = thermo(‘srk', temperature , pressure ); % using the UMR-PRU model
fluid_1.addComponent(‘CO2', 3.0);
luid_1.addComponent('methane', 90.0);
fluid_1.addComponent(‘ethane', 5.0);
fluid_1.addComponent(‘propane', 3.0);
fluid_1.createDatabase(1); % reading new parameters from database
fluid_1.setMixingRule(2); % using the mixing rule defined for UMR-PRU¨
GCV(fluid_1, 15, 15); % calculating gross calorific value 15C/15C
WI(fluid_1, 15, 15); % calculating wobbe index 15C/15C
reldens(fluid_1, 15); % calculating relative density at 15C

## Slide 53: Calculating water dew point (ISO 5198)
GERG-water EOS can be used to calculate water dew point according to ISO5198
The water dew point is calculated using the method: dewt_gw(fluidName)
pressure = 290.0; % pressure in bara
temperature = 283.15; % temperature in Kelvin
fluid_1 = thermo(‘srk', temperature , pressure ); % using the CPA-EoS
fluid_1.addComponent(‘CO2', 3.0);
luid_1.addComponent('methane', 90.0);
fluid_1.addComponent(‘ethane', 5.0);
fluid_1.addComponent(‘propane', 3.0);
fluid_1.addComponent(‘water', 30.0e-4); % adding 40 ppm water
fluid_1.createDatabase(1); % reading new parameters from database
fluid_1.setMixingRule(2); % using classic mixing rule with temperature dep. kij
dew_gw(fluid_1) % calculation water dew point with GERG-water model

## Slide 54: Process simulation in NeqSim
Process simulation of simple process plants can be dne in NeqSim.
Various unit operations such as:
  Straems
  Separators
  Compressors
  Valves
  Mixers, and more
Simple dynamic process simulations can be performed
The solution algorithms solves one unit operation at a time in a predfined sequence
After defining and connecting the unit operations – process simulation are run using the run() method

## Slide 55: Defining streams
Stream are connecting unit operations. A stream is defined from a fluid using the function: stream(fluidName);
Two typies of streams are defined: the equilibrium stream (at equilibrium at given T & P), and non-equilibrium stream difned by neqstream(fluidName) where the phases are no assumed to be in equilibrium
pressure = 10.0; % pressure in bara
temperature = 273.15; % temperature in Kelvin
fluid_1 = thermo('srk', temperature, pressure); % using the SRK-EoS
fluid_1.addComponent('methane', 1.0); % adding 1 mole/second of methane
fluid_1.addComponent('propane', 1.0); % adding 1 mole/second of propane
fluid_1.createDatabase(1); % reading new parameters from database
fluid_1.setMixingRule(2); % using classic mixing rule with kij
stream_1 = strream(fluid_1); % defining a stream
run(); % running the prossess simulation (flash stream)
stream_1.displayRsults(); % displaying reusults of stream
stream_1.getThermoSystem().getPhase(0).getZ() % read compressibility of gas phase of the stream

## Slide 56: Valves
A valve is made using the function: valve(inputStream, pressure out) where pressure out is in bara
The outlet pressure can also be set by the function setOutletPressure(pressure)
Cv, valve opening, etc can also be specified for the valve
The outlet stream from a valve is obtained using the function valve.getOutStream()
pressure = 10.0; % pressure in bara
temperature = 273.15; % temperature in Kelvin
fluid_1 = thermo('srk', temperature, pressure); % using the SRK-EoS
fluid_1.addComponent('methane', 1.0); % adding 1 mole/second of methane
fluid_1.addComponent('propane', 1.0); % adding 1 mole/second of propane
fluid_1.createDatabase(1); % reading new parameters from database
fluid_1.setMixingRule(2); % using classic mixing rule with kij
stream_1 = strream(fluid_1); % defining a stream
valve_1 = valve(stream_1, 5.0); % setting up a valve and setting 5 bar outlet pres
run(); % running the prossess simulation (flash stream)
valve_1.displayResult() % displaying results from valve simulation

## Slide 57: Separators and scrubbers
Separators are defined using the function separator(streamName)
A gas scrubber is defined using the function gasscrubber(streamName)
The separation efficiency can be spesified using the function: setEfficiency()
Dimension and internals of spearators and scrubbers can also be spesified
pressure = 10.0; % pressure in bara
temperature = 273.15; % temperature in Kelvin
fluid_1 = thermo('srk', temperature, pressure); % using the SRK-EoS
fluid_1.addComponent('methane', 1.0); % adding 1 mole/second of methane
fluid_1.addComponent(n-heptane', 1.0); % adding 1 mole/second of propane
fluid_1.createDatabase(1); % reading new parameters from database
fluid_1.setMixingRule(2); % using classic mixing rule with kij
stream_1 = stream(fluid_1); % defining a stream
valve_1 = valve(stream_1, 5.0); % setting up a valve and setting 5 bar outlet pres
separator_1 = separator(valve_1.getOutStream()) % defining a separator
run(); % running the prossess simulation (flash stream)
separator_1.getGasOutStream().displayResults() % displaying the gas from the separator

## Slide 58: Compressors and pumps
A compressor is defined using the function: compressor(streamName, outPressure)
A pump is made using the function pump(streamName)
The outlet pressure is set by setOutPressure(pressure)
The efficiency is set by the function: setEfficiency(efficiency)
The calculation type can be set to adiabatic, polytropic.
stream_1 = stream(fluid_1); % defining a stream
valve_1 = valve(stream_1, 5.0); % setting up a valve and setting 5 bar outlet pres
separator_1 = separator(valve_1.getOutStream()) % defining a separator
gasCompressor_1 = compressor(separator_1.getGasOutStream(), 10.0); % setting up a gas compressor
oilPump_1 = pump(separator.getOilOutStream()); % defining a pump
run(); % running the prossess simulation (flash stream)

## Slide 59: Heat exchangers, heater and coolers
A heater is defined using the function heater(streamName, outTemperature)
The duty can be read usng the function getDuty() -the reported duty will be in Watt
Alternatively the duty can be specified – and the outlet temperature calculated
A cooler is made in the same way as a heater
A heatexchanger can be defined using the function heatexchanger(stream 1, stream 2), and specifying U*A values
stream_1 = stream(fluid_1); % defining a stream
valve_1 = valve(stream_1, 5.0); % setting up a valve and setting 5 bar outlet pres
separator_1 = separator(valve_1.getOutStream()) % defining a separator
gasCompressor_1 = compressor(separator_1.getGasOutStream(), 10.0); % setting up a gas compressor
oilPump_1 = pump(separator.getOilOutStream()); % defining a pump
gasHeater_1 = heater(gasCompressor_1.getOutStream(), 100.0); % setting up a heater
run(); % running the process simulation (flash stream)
gasHeater_1.getDuty(); % reading duty of heater

## Slide 60: Mixers
A mixer is defined using the function mixer()
Streams are added to the mixer using the function addStream(streamName);
Any number of streams can be added to the mixer
stream_1 = stream(fluid_1); % defining a stream
valve_1 = valve(stream_1, 5.0); % setting up a valve and setting 5 bar outlet pres
separator_1 = separator(valve_1.getOutStream()) % defining a separator
gasCompressor_1 = compressor(separator_1.getGasOutStream(), 10.0); % setting up a gas compressor
oilPump_1 = pump(separator.getOilOutStream()); % defining a pump
gasHeater_1 = heater(gasCompressor_1.getOutStream(), 100.0); % setting up a heater
mixer_1 = mixer(); % creating a mixer
mixer_1.addStream(gasHeater_1.getOutStream()); % adding the gas stream
run(); % running the process simulation (flash stream)

## Slide 61: Resirculation streams
Resirculations stream are added in the same way as normal stream
The run() method is repeated until convergence is obtained (sucessive substitutuion and sequential solving)